## Slide 1: Will your next Pi Wars entry be a Walker?
Dr. Christopher Parrott
The challenges of multi-legged robots
Notes: Today I am going to be talking about the challenges of multi-legged robots, and what you need to think about if building one yourself for entry into PiWars

## Slide 2: Walkers
SpotMini [1]
Mantis [2]
Asimo [3]
RoboSimian [4]
Snake Monster [5]
You too can build a walking robot!
Notes: When you think of a walker, chances are robots like these come to mind
Seeing these may give the impression that these robots are hard for the average maker to build
Today I would like to show you that is not the case!
First let me give you a bit of background of how I got in to walking robots

## Slide 3: Walkers & Me
Started by modding walkers into the video game Total Annihilation
Joined the Lynxmotion forum and learnt to build my own hexapod
Went on to do a PhD in Robotics
Explored walkers in simulation
Recently been building walkers at work for inspecting water pipes

## Slide 4: Why a Walker?
Can move in any direction
Can adapt to rough ground
Body height, position and angle are adjustable
Lots of moving parts
Complex to control
Slower than other movement options
They’re Cool!!

## Slide 5: Deciding on a Walker
How many legs?
  Biped (two legs)
  Quadruped (four legs)
  Hexapod (six legs)
  Octopod (eight legs)
Number of joints per leg?
  3 minimum for spider-like
  6 minimum for biped-like
Walking on rough ground?
  Needs contact sensors in feet

## Slide 6: Joint Motors
Servos are ideal for joints!
Motor with built-in feedback loop
Goes to and stays at an angle you tell it to
Considerations

## Slide 7: Servo Options
Hobby Servos
  PWM controlled
  Proportional feedback only
  Hackable to add analog output for reading angle (or can buy)
Hitec Servo [6]
Servo Drivers
  Many options for up to 16 servos
  Fewer for more (no HATs yet)
  None have connections for extra pin of analog output servos
Adafruit Analog Feedback Servo [7]
Sparkfun Pi Servo HAT [8]
Lynxmotion SSC-32U [9]

## Slide 8: Servo Options
Smart Servos
  Specifically designed for robotics
  Built-in PID feedback loop
  On a communication bus
  Can read angle, current, temp etc
ODrive [13]
Mechaduino [12]
DIY Servos
  Motor + Encoder + Driver + Microcontroller
  Off-the-shelf options available
Dynamixel [10]
Lynxmotion SS [11]

## Slide 9: Hardware Tips
Calibrate your servos!
  -90 and +90, and 0 degree values
  If your robot is heavy, calibrate upside down or under load
Go for metal gear servos if possible
Add springs to legs to reduce load
Place heaviest parts at the centre

## Slide 10: How to Walk
How to move each leg to touch a position in space
How to move those positions in a way that creates walking
How to stay balanced (optional)

## Slide 11: Inverse Kinematics (IK)
Find the joint angles of a leg that place its end at a target
3 joints has 2 solutions (under and over)
Higher joint counts have many more!
  Find one by grouping joints together
  Or add directions for some to aim in
Solvable with Trigonometry!

## Slide 12: Gait (Walking Pattern)
A repeating cycle of steps that are taken by a set of legs to achieve movement in a direction
Biped
Quadruped

## Slide 13: Gait Generation
Convert a gait to offsets for each leg’s idle target position

## Slide 14: Balancing
Dynamic
Static
Make continual corrections to avoid falling over
Move robot’s centre to be within the legs that are on the ground

## Slide 15: Will your next Pi Wars entry be a Walker?
Highly recommended if you are looking for a new challenge!
Will learn new things about robotics and get a cool new robot
To get you started my walking simulator is now on Github!
May make a custom HAT that does everything onboard too

## Slide 16: Thanks for listening!
Twitter: @ZodiusInfuser
YouTube: youtube.com/user/ZodiusInfuser
Website: zodiusinfuser.uk

## Slide 17: Image References
[1] https://www.businessinsider.com/boston-dynamics-spot-robot-dog-going-on-sale-this-year-2019-6
[2] https://www.qimtek.co.uk/news/applied-measurements-submersible-load-cells-fitted-world-s-largest-all-terrain-hexapod
[3] https://spectrum.ieee.org/automaton/robotics/humanoids/humanoid-robots-rise
[4] https://scienceandtechnology.jpl.nasa.gov/research/research-topics-list/spacecraft-technologies/mobility-robotics
[5] https://www.cmu.edu/news/stories/archives/2015/january/reconfigurable-modular-robots.html
[6] http://www.modelshopleeds.co.uk/catalog/product_info.php?products_id=864
[7] https://www.adafruit.com/product/1449
[8] https://www.sparkfun.com/products/14328
[9] https://www.robotshop.com/uk/lynxmotion-ssc-32u-usb-servo-controller.html
[10] https://robosavvy.com/store/robotis-dynamixel-ax-12a.html
[11] http://www.lynxmotion.com/p-1126-lynxmotion-smart-servo-lss-motor-standard-st1.aspx
[12] https://tropical-labs.com/shop/mechaduino-0-2-servo/
[13] https://odriverobotics.com/